## Slide 1: Principles of Computer Architecture
CSE 240A
Fall 2024
Hadi Esmaeilzadeh
hadi@ucsd.edu
University of California, San Diego
Notes: Color code: 6699CC, 3399CC

## Slide 2: Revisiting Branch Hazard Solutions
Stall
Predict Not Taken
Predict Taken
Branch Delay Slot
This is kind of an odds-and-ends lecture. We’ll be finishing up a few things, making pipelining a little more real – dealing with some aspects that aren’t quite as clean as it may have looked last lecture…
Notes: This is kind of an odds-and-ends lecture. We’ll be finishing up a few things, making pipelining a little more real – dealing with some aspects that aren’t quite as clean as it may have looked last lecture…

## Slide 3: Predict Not Taken
Branch
I+1
I+2
I+3
IF
ID
IF
Branch
I+1
Branch Target
T+1
IF
ID
IF
branch not taken
branch taken

## Slide 4: Predict Not Taken
Branch
I+1
I+2
I+3
IF
ID
EX
MEM
WB
IF
(bubble)
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Branch
I+1
Branch Target
T+1
IF
ID
EX
MEM
WB
IF
ID
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
branch not taken
branch taken
(bubble)
(bubble)
(bubble)

## Slide 5: Delayed Branch
Branch
I+1 (delay slot)
I+2
I+3
IF
ID
IF
Branch
I+1 (delay slot)
Branch Target
T+1
IF
ID
IF
branch not taken
branch taken

## Slide 6: Delayed Branch
Branch
I+1 (delay slot)
I+2
I+3
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Branch
I+1 (delay slot)
Branch Target
T+1
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
branch not taken
branch taken

## Slide 7: Filling the delay slot (e.g., in the compiler)
Can be done when?
Improves performance when?
lw R1, 10000(R7)
add R5, R6, R1
beqz R5, label:
sub R8, R1, R3
add R4, R8, R9
and R2, R4, R8
add R2, R5, R8
label:
Could do sub with register rename
OR…..
This one is okay

## Slide 8: Problems filling delay slot
1. need to predict __________ of branch to be most effective
2. limited by ______________ restriction
direction
correctness

## Slide 9: Problems filling delay slot
1. need to predict __________ of branch to be most effective
2. limited by ______________ restriction
____________ restriction can be removed by a canceling branch
  branch likely (or branch not likely???)
  e.g.,
  beqz likely
  delay slot instruction
  fall-through instruction
squashed/nullified/canceled if branch not taken
correctness

## Slide 10: Branch Likely
Branch likely
I+1 (delay slot)
I+2
I+3
IF
ID
EX
MEM
WB
IF
(bubble)
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Branch likely
I+1 (delay slot)
Branch Target
T+1
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
branch not taken
branch taken
(bubble)
(bubble)
(bubble)

## Slide 11: Delay Slot Utilization
18% of delay slots left empty
11% of delay slots (1) use canceling branches and (2) end up getting canceled
Data from real MIPS – 29% of
Branch Delay Slot’s useless.
Find source…

## Slide 12: Delay Slots, the scorecard
Pros
Cons
Would you include branch delay slots in your ISA if you made one today?
A. Yes B. No
Maybe cheaper for hw (no flushing)
Compiler finds useful insts
If good sked, no branch hazards
Could be not useful dep. On sked
If cancelling, not prediction…
Breaks level of abstraction!!

## Slide 14: Static Branch Prediction
Static branch prediction takes place at compile time, dynamic branch prediction during program execution
Typically requires some ISA support (eg branch_likely)
static bp done by software, dynamic bp done in hardware
How to make static branch predictions?
Static branch prediction enables
  more effective code scheduling around hazards (how?)
  more effective use of delay slots
Spec92, profile-driven
static prediction.
Schedule for more likely
hazards.

## Slide 15: Static Branch Prediction
What’s might be an obstacle to doing static branch prediction (i.e., having the compiler denote which branches are biased taken/not-taken)?
Profiling (can you trust?)
Branch has diff behavior!
Breaks abstraction:
Compiler knows issue
Opcode implicit message
Change ISA for this

## Slide 16: MIPS 5-stage Integer Pipeline Performance
Only stalls for load hazards and branch hazards, both of which can be reduced (but not eliminated) by software
segue

## Slide 17: But now, the real world interrupts...
Pipelining is not as easy as we have made it seem so far...
  interrupts and exceptions
  long-latency instructions

## Slide 18: Exceptions and Interrupts
Transfer of control flow (to an exception handler) without an explicit branch or jump
are often unpredictable
examples
  I/O device request
  OS system call
  arithmetic overflow/underflow
  FP error
  page fault
  memory-protection violation
  hardware error
  undefined instruction

## Slide 19
Which of the following events are synchronous (consistently occur at the same time in a program given the same input and same memory allocation)
Selection | Synchronous
A | 1, 3, 4
B | 1, 2
C | 2,3
D | 3,4
E | None of the above
ALU overflow exception
unconditional branch
timer interrupt
I/O interrupt
Notes: Correct B: 1 and 2

## Slide 20: Classes of Exceptions
synchronous vs. asynchronous
user-initiated vs. coerced
user maskable vs. nonmaskable
within instruction vs. between instructions
resume vs. terminate
Diff based on OS
(Doom vs. space shuttle)

## Slide 21: Basic Exception Methodology
What do you need to do?
Save the reason, change PC. For the OS, save program state
Notes: Save the reason, change PC (discuss vectored vs.
Cause register). For the OS, save program state

## Slide 22: Basic Exception Methodology
turn off writes for faulting instruction and following
force a trap into the kernel at the next IF
save the cause in a register OR go to a specific place in the kernel based on the cause
save the PC of the faulting instruction

## Slide 23
When an exception occurs, for which type of instruction is saving only the current pc insufficient for the OS to resume execution of the program later.
Branch
Jump and link
Delayed branch
Load Word
More than one of the above
Notes: Answer: Delayed Branch

## Slide 24: Exceptions Can Occur In Several Places in the pipeline
IF -- page fault on memory access, misaligned memory access, memory-protection violation
ID -- illegal opcode
EX -- arithmetic exception
MEM -- page fault, misaligned access, memory-protection
WB -- none
(and, of course, asynchronous can happen anytime)
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
LW
ADD
SUB

## Slide 25: Simplifying Exceptions in the ISA
Each instruction changes machine state only once
  autoincrement
  string operations
  condition codes
Each instruction changes machine state at the end of the pipeline (when you know it will not cause an exception)
Enables precise interrupts
string ops are rough?
***segue***

## Slide 26: But now, the real world interrupts...
Pipelining is not as easy as we have made it seem so far...
  interrupts and exceptions
  long-latency instructions

## Slide 27: Handling Multicycle Operations
Unrealistic to expect that all operations take the same amount of time to execute
___, some _______________will take longer
This violates some of the assumptions of our simple pipeline
fp
Memory ops

## Slide 28: Multiple Execution Pipelines
FU Latency Initiation interval
Integer 0 1
Memory 1 1
FP add 3 1
FP multiply 6 1
FP divide 24 24
What new problems are introduced?

## Slide 29
Which problems are introduced by variable length pipelines?
Selection | Now a problem
A | 1, 2, 3
B | 1, 2, 4
C | 2, 3
D | 1, 3, 4
E | None of the above
Structural hazards
WAR Hazards
WAW Hazards
Out of order completion
Notes: WAR are not possible yet
WAW hazards appear
Out of order compeetion
1, 3, 4 are correct -> D is correct

## Slide 30: New problems
structural hazards are ___Yes_____
  divide unit
  WB stage
WAW hazards are __Yes___
out-of-order completion is ___Yes____
WAR hazards are _____No_____
Yes to all except WAR (not yet)

## Slide 31: Structural hazards and WAW hazards
structural hazards
  divide unit
  WB stage
WAW hazards
ADDD IF ID A1 A2 A3 A4 MEM WB
... IF ID EX MEM WB
... IF ID EX MEM WB
LD IF ID EX MEM WB
ADDD F8, ... IF ID A1 A2 A3 A4 MEM WB
LD F8, ... IF ID EX MEM WB

## Slide 32
Which of the following becomes much more complicated if we have out-of-order completion?
Selection | Now a problem
A | Branches
B | Exceptions
C | Both
D | Neither
Notes: Correct Answer -> C
Exceptions are terrible,
branches are tough too, depending
on resolution, show branch
followed by sw

## Slide 33: New problems
structural hazards
  divide unit
  WB stage
WAW hazards are possible
out-of-order completion
WAR hazards still not possible

## Slide 34: New problems
structural hazards
  divide unit
  WB stage
WAW hazards are possible
out-of-order completion
WAR hazards still not possible
(We’ll ignore solutions to these problems, for now, because our architecture for out-of-order execution will subsume those solutions)

## Slide 35: Key Points
Data Hazards can be significantly reduced by forwarding
Branch hazards can be reduced by early computation of condition and target, branch delay slots, branch prediction
Data hazard and branch hazard reduction require complex compiler support
Exceptions are hard
variable-length instructions introduce structural hazards, WAW hazards, more RAW hazards