## Slide 1: Principles of Computer Architecture
CSE 240A
Fall 2024
Hadi Esmaeilzadeh
hadi@ucsd.edu
University of California, San Diego
Notes: Color code: 6699CC, 3399CC

## Slide 2: Branch Prediction
or
sometimes you just have to guess

## Slide 3: Looking for Instruction Level Parallelism (ILP)
We want to identify and exploit ILP – instructions that can potentially be executed at the same time.
Branches are 15-20% of instructions
  Implications?
Can only keep the pipeline full if we can consistently keep fetching well past unresolved branches.
Can only exploit high levels of parallelism if we consistently have multiple basic blocks in the processor at once.
Lots of branches
Small basic blocks

## Slide 4: Importance of Branch Prediction
MIPS R2000 -- branch hazard of 1 cycle, 1 instruction issued per cycle
  delayed branch
next generation – 2-3 cycle hazard, 1-2 instructions issued per cycle
  cost of branch misprediction goes up
Pentium 4

## Slide 5: Importance of Branch Prediction
Branch fetched
4-wide superscalar
20-stage pipeline
Notes: Show resolved, show corrected

## Slide 6: Branch Prediction
Easiest (static prediction)
  always not taken, always taken
  forward not taken, backward always taken
  compiler predicted (branch likely, branch not likely)
Question next..., then dynamic

## Slide 7: Branch Prediction
Easiest (static prediction)
  always not taken, always taken
  forward not taken, backward always taken
  compiler predicted (branch likely, branch not likely)
What's the problem with static prediction?
Selection | Problem
A | Requires ISA change
B | Limited by branches bias
C | Both
D | Neither
Notes: Correct answer C
For B, remember the branches with 51% bias vs 99% bias

## Slide 8: Branch Prediction
for(int i = 0; i<n; i++) {
if(i % 2 == 0) {
blah;
}
else {
foo;
}
}
Are we entirely stuck?
Notes: The branch is 50% taken
This can be separated to two independent loops
For (i=0, i< n, I +=2)
blah
For(i=1; i<n; +=2)
foo

## Slide 9: Branch Prediction
Easiest (static prediction)
  always not taken, always taken
  forward not taken, backward always taken
  compiler predicted (branch likely, branch not likely)
What's else could you do to help the compiler?
Restructure code, profile code.
Less likely, use value range propagation.

## Slide 10: Branch Prediction
Easiest (static prediction)
  always not taken, always taken
  forward not taken, backward always taken
  compiler predicted (branch likely, branch not likely)
Static prediction is limited.
Dynamic branch prediction

## Slide 11: Dynamic Branch Prediction
What can we use to predict outcomes?

## Slide 12: Branch Prediction
Easiest (static prediction)
  always not taken, always taken
  forward not taken, backward always taken
  compiler predicted (branch likely, branch not likely)
Next easiest (1-bit dynamic)
  remember last taken/not taken per branch (1 bit)
  per branch approximated
    per I cache line
    use part of address
  what happens on a loop?
for (i=0;i<5;i++) { loop: …
… …
} bnez r1, loop:

## Slide 13: Paper Reading
Lets’ put this in context that this work created a
HUGE area of research.

## Slide 14: Context
What makes this interesting, for those who are well acquainted with branch prediction already…
Before pipelined machines, branches were not problematic
This paper has no real context in terms of prior work on branch prediction
We get to see Jim Smith working through the first set of reasonable choices.

## Slide 15: Branch Predictor Strategies
Strategy 1: Predict that all branches will be taken.
  Strategy la: Predict that only certain branch operation codes will be taken.
Strategy 2: Always predict that a branch will be decided as on its last execution.
Strategy 3: Predict that only backward branches will be taken.
Strategy 4: Maintain a table of the m most recent branches not taken. Predict that only branches found in table will be not taken.
Strategy 5: Maintain a history bit in cache and predict according to the history bit in cache and predict according to the history bit (a 64-word instruction cache was used).
Strategy 6: Hash the branch address to m bits and access a 2m word RAM containing history bits, and predict according to the history bit.
Strategy 7: Like Strategy 6, but use counters instead of a single history bit.

## Slide 16: Branch Confidence
In the paper, branch confidence is suggested as a technique to avoid a high-cost penalty of having mispredicted and fetched the wrong path, rather than doing nothing. Such a penalty is not applicable today, but this idea has been re-examined more recently, why?
Throttle fetch on poor confidence

## Slide 17: 1-bit branch prediction
1
0
1
program counter
Selection | Accuracy
A | 50%
B | 60%
C | 80%
D | 100%
E | None of the above
For a 1-bit predictor and a branch whose pattern is:
TTTTN
What will it's prediction accuracy be (over many, many executions, assume no aliasing)?
Notes: Too easily swaye:
Consider the second iterations of the loop
TTTTNTTTTN
Correct answer is B, 60%

## Slide 18: 1-bit branch prediction
1
0
1
program counter
Selection | Accuracy
A | 0%
B | 25%
C | 50%
D | 100%
E | None of the above
For a 1-bit predictor and a branch whose pattern is:
TNTNTN
What will it's prediction accuracy be (over many, many executions, assume no aliasing)?

## Slide 19: 2-bit branch prediction
Strongly Taken
11
Weakly Taken
10
Weakly Not Taken
01
Strongly Not Taken
00
Decrement when not taken
Increment when taken
Saturating counter
00
01
10
11
Notes: There

## Slide 20: 2-bit branch prediction
Often referred to as a “saturating counter”
Loops?
Strongly Taken
11
Weakly Taken
10
Weakly Not Taken
01
Strongly Not Taken
00
Decrement when not taken
Increment when taken
Saturating counter
for (I=0;I<5;I++) { loop: …
… …
} bnez r1, loop:

## Slide 21: Bimodal Predictor
has limited size
2 bits by N (e.g. 4K)
uses low bits of branch address to choose entry
branch address
00
BHT
Why low bits?

## Slide 22: 2-bit branch prediction
Selection | Accuracy
A | 50%
B | 60%
C | 80%
D | 100%
E | None of the above
For a 2-bit predictor and a branch whose pattern is:
TTTTN
What will it's prediction accuracy be (over many, many executions, assume no aliasing)?
branch address
??
BHT
Notes: The correct answer is 80% D
Look at the second iteration
TTTTNTTTTN
ST, ST, ST, ST, WT, ST… Only ne misprediction instead of two

## Slide 23: 2-bit branch prediction
Selectionx | Better
A | 0%
B | 25%
C | 50%
D | 75%
E | None of the above
For branches with the following pattern:
TNTNTN
How much better will the 2-bit predictor do on average than the 1-bit predictor?
branch address
??
BHT
Notes: Walk through all starts, either
0% or 50%, actual correct
is ~38%
Correct answer is E none of the above:
TNTNTN
00 M,C,M,C,M => 50%
01 M,M,M,M,M => 0%
10 C,M,C,M,C => 50%
11 C,M,C,M,C,C => 50%
150% + 0% / 4 => 37.5%
0, M, M,M,M
1 C,M,M,M,M for long iterations can be approximated with 0 percent

## Slide 24: 2-bit branch prediction
Selection | Effect
A | The aliasing is detected, the old value is cleared, and we restart for the new branch
B | The aliasing is allowed and interference may occur
C | The aliasing is allowed only if the two branches have the same bias
D | A new set of bits are chosen to determine a new hash function
E | None of the above
What happens when the low order bits map to the same location in the BHT?
branch address
00
BHT
Notes: A,C,D – I wish.
B is a real problem
B is the correct answer

## Slide 25: 2-bit prediction accuracy
Is this good enough?