## Slide 1: Principles of Computer Architecture
CSE 240A
Fall 2024
Hadi Esmaeilzadeh
hadi@ucsd.edu
University of California, San Diego
Notes: Color code: 6699CC, 3399CC

## Slide 2: Branch Prediction
or
sometimes you just have to guess

## Slide 3: 2-bit prediction accuracy
Is this good enough?

## Slide 4: Can We Do Better?
Can we get more information dynamically than just the general history of this branch?

## Slide 5: Can We Do Better?
Can we get more information dynamically than just the general history of this branch?
We can look at patterns (local predictor) for a particular branch.
  last eight branches 00100100, then it is a good guess that the next one is “1” (taken)
even/odd branch?
000000
111111
001001
000000
address
BHT
00
00
11

## Slide 6: Can We Do Better?
For a local predictor and a branch whose pattern is:
TNTNTNTN
What will it's prediction accuracy be (over many, many executions, assume no aliasing)?
000000
111111
001001
000000
address
BHT
00
00
11
Selection | Accuracy
A | ~50%
B | ~75%
C | ~100%
D | Can't tell from the information provided
Notes: The PC will be mapping to the same location
But the pattern in that location will be alternating between
010101 -> 11
101010 -> 00
That are mapped to completely separate locations

## Slide 7
Illustrating branch predictors

## Slide 8: 1-bit BHT
1
0
1
program counter
for (i=0;i<10;i++) {
...
...
}
...
...
subi $i, $i, #1
bnez $i, loop
1st iteration
Branch Taken
(predicted not taken)
History -> 1
Notes: Initialized with NT -> Misprediction

## Slide 9: 1-bit BHT
1
1
1
program counter
2nd iteration
Branch Taken
(predicted taken)
History -> 1
for (i=0;i<10;i++) {
...
...
}
...
...
subi $i, $i, #1
bnez $i, loop
Notes: Correct prediction

## Slide 10: 1-bit BHT
1
1
1
program counter
3rd iteration
Branch Taken
(predicted taken)
History -> 1
for (i=0;i<10;i++) {
...
...
}
...
...
subi $i, $i, #1
bnez $i, loop
Notes: Misprediction

## Slide 11: 1-bit BHT
1
1
1
program counter
10th iteration
Branch Not Taken
(predicted taken)
History -> 0
for (i=0;i<10;i++) {
...
...
}
...
...
subi $i, $i, #1
bnez $i, loop

## Slide 12: 1-bit BHT
1
0
1
program counter
1st iteration again
Branch Taken
(predicted not taken)
History -> 1
for (i=0;i<10;i++) {
...
...
}
...
...
subi $i, $i, #1
bnez $i, loop
Notes: Coming back to the second time we are executing the loop
We will have another misprediction

## Slide 13: 2-bit Branch History Table
branch address
01
BHT
1st iteration
Branch Taken
(predicted not taken)
History -> ?
Notes: Misprediction
History will be updated to 10

## Slide 14: 2-bit Branch History Table
branch address
10
BHT
2nd iteration
Branch Taken
(predicted taken)
History -> ?

## Slide 15: 2-bit Branch History Table
branch address
11
BHT
3rd iteration
Branch Taken
(predicted taken)
History -> ?
Notes: Correct prediction

## Slide 16: 2-bit Branch History Table
branch address
11
BHT
10th iteration
Branch Not Taken
(predicted taken)
History -> ?
Notes: Misprediction -> The history is going to change to 10

## Slide 17: 2-bit Branch History Table
branch address
10
BHT
1st iteration again
Branch Taken
(predicted taken)
History -> ?
Notes: Second time we are executing the entire loop
Then we have correct prediction and the history is updated to 11

## Slide 18: Local predictor
000000
111111
011011
000000
address
BHT
00
01
11
Pattern
History
Table
Assume a loop that repeatedly executes three iterations (thus, the
branch is TTNTTNTTN…
First iteration
Branch Taken
Predicted not taken
BHT -> 10
Pattern Hist Table -> 101101
01
Entry
011011
101101
110110
01
01
Notes: Push 1 from left to the entry in 011011
Mispredict and push the 1 frm left and update the BHT to 10

## Slide 19: Local predictor
000000
111111
101101
000000
address
BHT
00
10
11
Pattern
History
Table
Assume a loop that repeatedly executes three iterations (thus, the
branch is TTNTTNTTN…
Second iteration
Branch Taken
Predicted not taken
BHT -> 10
Pattern Hist Table -> 110110
01
Entry
011011
101101
110110
01
01
Notes: 101101
The BHT in that location is 01 -> Mipredict and update to 10

## Slide 20: Local predictor
000000
111111
110110
000000
address
BHT
00
10
11
Pattern
History
Table
Assume a loop that repeatedly executes three iterations (thus, the
branch is TTNTTNTTN…
Third iteration
Branch not taken
Predicted not taken
BHT -> 00
Pattern Hist Table -> 011011
01
Entry
011011
101101
110110
10
01
Notes: 110110
Correct prediction -> It should not be taken and the BHT is decremented to 00

## Slide 21: Local predictor
000000
111111
011011
000000
address
BHT
00
10
11
Pattern
History
Table
Assume a loop that repeatedly executes three iterations (thus, the
branch is TTNTTNTTN…
First iteration, again
Branch taken
Predicted taken
BHT -> 11
Pattern Hist Table -> 101101
01
Entry
011011
101101
110110
10
00
Notes: 011011 -> Correct prediction -> updated to 11

## Slide 22: Local predictor
000000
111111
101101
000000
address
BHT
00
11
11
Pattern
History
Table
Assume a loop that repeatedly executes three iterations (thus, the
branch is TTNTTNTTN…
Second iteration, again
Branch taken
Predicted taken
BHT -> 11
Pattern Hist Table -> 110110
01
Entry
011011
101101
110110
10
00
Notes: Correct prediction -> BHT is updated to 11

## Slide 23: Local predictor
000000
111111
110110
000000
address
BHT
00
11
11
Pattern
History
Table
Assume a loop that repeatedly executes three iterations (thus, the
branch is TTNTTNTTN…
Third iteration, again
Branch not taken
Predicted not taken
BHT -> 00
Pattern Hist Table -> 011011
01
Entry
011011
101101
110110
11
00
Notes: Correct prediction, not taken and the BHT is not updated

## Slide 24: Local predictor
000000
111111
011011
000000
address
BHT
00
11
11
Pattern
History
Table
Assume a loop that repeatedly executes three iterations (thus, the
branch is TTNTTNTTN…
First iteration, yet again
Branch taken
Predicted taken
BHT -> 11
Pattern Hist Table -> 101101
01
Entry
011011
101101
110110
11
00
Notes: Correct prediction of taken and the BHT is constnt

## Slide 25: This seems great!
Is this just better then? When might it do well, and when might it struggle?
000000
111111
001001
000000
address
BHT
00
00
11
Two ways to alias
Long time to train

## Slide 26: Can We Do Better?
Correlating Branch Predictors also look at other branches for clues
  if (i == 0)
  ...
  if (i > 7)
  ...
Often use two indices
  Global history register (GHR) --> history of last m branches (e.g., 0100011)
  branch address
If (I < 10) j = 5;
If (j == 5) blah;

## Slide 27: Correlating Branch Predictors
The global history register is a shift register that records the last n conditional branches (of any address) encountered by the processor.
ghr
2-bit predictors
00
01
11
00
BHT

## Slide 28: Yeh and Patt Alternative Implementations of Two Level Adaptive Branch Prediction

## Slide 29: Yeh and Patt
Described and evaluated some of these same predictors, although their terminology didn’t stick.
000000
111111
011011
000000
address
BHT
00
01
11
Pattern
History
Table
01
Entry
011011
101101
110110
01
01
ghr
2-bit predictors
00
01
11
00
BHT
Local Predictor == PAg
Correlating Predictor == GAg

## Slide 30: Yeh and Patt
What conclusions do they come to?
They like saturating counter vs other state machines
- mention automaton A1 appeared in prior text
Versions, came from a Patterson paper.
They like 2-level adaptive (local)

## Slide 31: Yeh and Patt
What conclusions do they come to?
How do you handle context switches?
Do nothing.
Impact on perf is minimal.
State of old program likely to be better than some iniitialized state.

## Slide 32: Two-level correlating branch predictors
Can use both the PC address and the GHR
If the combining function is xor, this is called the _________ predictor.
ghr
2-bit predictors
00
01
11
00
PC
combining
function
BHT
Notes: This is called the gshare

## Slide 33: Gshare
For a gshare predictor and a branch whose pattern is:
TNTNTNTN
What will it's prediction accuracy be (over many, many executions, assume no aliasing)?
Selection | Accuracy
A | ~50%
B | ~75%
C | ~100%
D | Can't tell from the information provided
ghr
2-bit
predictors
00
01
11
00
PC
combining
function
BHT
Notes: C is the correct answer
010101 -> 00 100% accuracy
101010 -> 11
D is also acceptable because we don’t know the PC and some of the aliasing that might happen

## Slide 34: Performance of 2-level Correlating Branch Prediction

## Slide 35: Are we happy yet????