## Slide 1: Principles of Computer Architecture
CSE 240A
Fall 2024
Hadi Esmaeilzadeh
hadi@ucsd.edu
University of California, San Diego
Notes: Color code: 6699CC, 3399CC

## Slide 2: Branch Prediction
or
sometimes you just have to guess

## Slide 3: Are we happy yet????

## Slide 4: More BP performance

## Slide 5: Are we happy yet????
Combining branch predictors or tournament predictors use multiple schemes and a voter to decide which one typically does better for that branch.
PC
P1
P2
use P2

## Slide 6: But hang on a sec...
When do we need to do the prediction to avoid any control hazards on a correct prediction?
A taken/not taken prediction only helps us if....?

## Slide 7: Branch Target Buffers
predict the location of branches in the instruction stream
predict the destination of branches

## Slide 8: BTB Operation
use PC (all bits) for lookup
  match implies this is a branch
if match and predict bits => taken, set PC to predicted PC
if branch predict wrong, must recover (same as branch hazards we’ve already seen)
  but what about dynamically scheduled (out of order) processor??
if decode indicates branch when no BTB match, two choices:
  look up prediction now and act on it
  just predict not taken
when branch resolved, update BTB (at least prediction bits, maybe more)

## Slide 9: Can we use this for prediction?
There's an idea to clean up the logic and reduce aliasing by just keeping the prediction bits in the BTB. Is this a good idea?
Selection | Good idea?
A | Yes
B | No
Notes: Correct answer B
Big problem, replacement. This is a small table and it not enough to hold all the information.
Minor problem: bias loss.
But not a bad place to put stuff entirely…

## Slide 10: BTB Performance
Two things that can go wrong
  didn’t predict the presence of branch (misfetch)
  mispredicted a branch (mispredict)
Can use (now, always use) both BTB and branch predictor
  have no prediction bits in BTB
  presence of PC in BTB indicates a lookup in branch predictor to predict whether the branch will go to destination address in BTB.

## Slide 11: What about indirect jumps/returns?
Branch predictor does really well with conditional jumps
BTB does really well with unconditional jumps (jump, jal, etc.)
Indirect jumps often jump to different destinations, even from the same instruction. Indirect jumps most often used for return instructions. Sometimes used for case. Heavily used in object-oriented languages.
Return easily handled by a stack.
  jal -> push PC+4
  return -> predict jump to address on top of stack, pop stack
  Most processors include a hardware return address stack (RAS), used only for prediction.

## Slide 12: Real BP -- PowerPC 620
256-entry 2-way set-associative BTB
2048-entry BHT indexed by PC
return-address stack

## Slide 13: Power 4
Up to 2 branches per cycle predicted
PC GHR
16K
16K
16K
XOR
BHT gshare chooser (use bht or gshare result?)

## Slide 14: Pentium Pro
512-entry BTB 4-way set-associative
2-level predictor (1st level in BTB, one per set, 4 bits)
return stack
branch PC
target
branch PC
target
branch
pattern
BHT

## Slide 15: Compaq/Digital Alpha 21264
PC
10
3
2
2
GHR
12
Local Predictor
Global
Predictor
Chooser
Branch Prediction
next-cache-line field in I-cache replaces BTB
return address stack
10

## Slide 16: The YAGS Branch Prediction Scheme A. N. Eden and T. Mudge,
What’s the big problem they are trying to solve
What does aliasing do to the predictor?
What are some general techniques to reduce the impact of aliasing?
Only predict some (remove bias)
Create different hash functions
Group by bias

## Slide 17: Aliasing
Constructive
Neutral
Destructive
How does the two-level local predictor do wrt aliasing?
21264 tournament predictor?

## Slide 18: Local predictor aliasing?
000000
111111
001001
000000
address
BHT
00
00
11

## Slide 19: 21264 Aliasing?
PC
10
3
2
2
GHR
12
Local Predictor
Global
Predictor
Chooser
Branch Prediction
10

## Slide 20: Anti-Aliasing Predictors

## Slide 21: Anti-Aliasing Predictors

## Slide 22: Anti-Aliasing Predictors

## Slide 23: Case Study
Creating Artificial Global History to Improve Branch Prediction Accuracy.
Leo Porter, and Dean M. Tullsen.
In Twenty-Third International Conference on Supercomputing, June, 2009.
Accurate Branch Prediction for Short Threads.
Bumyong Choi, Leo Porter, and Dean M. Tullsen.
In Thirteenth International Conference on Architectural Support for Programming Languages and Operating Systems, March, 2008.

## Slide 24: Rapid Migration
Core Hopping for thermal
Thread scheduling for Heterogeneous Cores
Hardware-based load balancing on CMP of SMTs
Speculative Multithreading (SpMT)
Core 0
Core 1

## Slide 25: For SpMT the GHR is unknown
CQIP
P0 P1
SP
GHR= ????
Notes: Segue – but, in the SpMT scenario, we do not know the correct GHR when we spawn a new thread.

## Slide 26: A meaningful GHR value (Oracle)
CQIP
P0 P1
SP
GHR= NT…NN
Notes: Segue – but, in the SpMT scenario, we do not know the correct GHR when we spawn a new thread.

## Slide 27: Policy = PC
CQIP
P0 P1
SP
GHR= PC(CQIP) >> 2

## Slide 28: Overall – A puzzle

## Slide 29
Prior work has shown that a large percentage of branches correlate with a relatively small number of prior branches (Evers ‘98)
If x values are consistent, predictors learn.
Branch Correlation
00
PHT
branch address
0xxx1xx1
GHR
Consistent

## Slide 30
If x values are uncorrelated and inconsistent, predictors may access more table entries causing slow learning and aliasing becomes more likely.
Branch Correlation
01
PHT
branch address
0xxx1xx1
GHR
Noise
Notes: Key word here is 32x as many entries as needed.

## Slide 31
If this branch entirely lacks correlation (all noise), the predictors learn slowly and aliasing becomes more likely.
University of California, San Diego
Branch Correlation
01
PHT
branch address
xxxxxxxx
GHR
Noise

## Slide 32: An experiment
Analyzed branch prediction using 2-bit predictors per unique history per branch
Similar to infinite gshare with no aliasing
Compared the accuracy of branch bias against the accuracy of the non-aliasing infinite gshare predictor
  75% biased but 90% accuracy with history
  75% biased but 50% accuracy with history
Notes: Give an example of both positive and negative

## Slide 33: Global History Benefit
Diminishing Returns
Increasing Negative Impact
Gshare/
filter
More modern predictors try to
Get more history, without the
Detriment. Positive is limited to gshare, could do better
Notes: Mention lengths have been increasing with recent implementations
Ideal goal is to decrease negative impact while retaining positive impact

## Slide 34: Branch Prediction Key Points
Significant improvement in predictor accuracy overshadowed by increases in pipeline depth and superscalar width.
2-bit predictors capture tendencies well.
Correlating predictors improve accuracy, particularly when combined with 2-bit predictors.
Accurate branch prediction does no good if we don’t know there was a branch to predict
BTB identifies branches in (or before) IF stage.
BTB combined with branch prediction table identifies branches to predict, and predicts them well.
Modern codes can create significant aliasing in branch predictor tables.